## Slide 1: Serial Interrupt Programming

## Slide 2: Find the TH1 value needed to have the following baud rates. (a) 9600 (b) 4800 (c) 2400 (d) 1200
XTAL = 11.0592 MHz
The machine cycle frequency of 8051 = 11.0592 / 12 = 921.6 kHz, and 921.6 kHz / 32 = 28,800 Hz is frequency by UART to timer 1 to set baud rate.
  (a) 28,800 / 3 = 9600
  (b) 28,800/6 = 4800
  (c) 28,800 / 12 = 2400
  (d) 28,800 / 24 = 1200
Time period of each clock tick: T0 = 1/f = 1/28800
Duration of timer: n*T0 (n is the number of clock ticks)
1/9600 = n*T0 = n*1/28800 = 28800/9600 = 3
TH1 =FD

## Slide 3
Baud Rate | TH1 (Decimal) | TH1(Hex)
9600 | -3 | FD
4800 | -6 | FA
2400 | -12 | F4
1200 | -24 | E8

## Slide 4: Transfer Character
1. TMOD register is loaded with the value 20H, indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set the baud rate
2. The TH1 is loaded with one of the values to set the baud rate for serial data transfer
3. The SCON register is loaded with the value 50H, indicating serial mode 1, where an 8- bit data is framed with start and stop bits
4. TR1 is set to 1 to start timer 1
5. TI is cleared
6. The character byte to be transferred serially is written into the SBUF register
7. The TI flag bit is monitored to see if the character has been transferred completely
8. To transfer the next byte, go to step 5

## Slide 5: Receive Character
TMOD register is loaded with the value 20H, indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set baud rate
2. TH1 is loaded to set baud rate
3. The SCON register is loaded with the value 50H, indicating serial mode 1, where an 8- bit data is framed with start and stop bits
4. TR1 is set to 1 to start timer 1
5. RI is cleared
6. The RI flag bit is monitored to see if an entire character has been received yet
7. When RI is raised, SBUF has the byte
8. To receive the next character, go to step 5

## Slide 6
SCON
IE

## Slide 7: Program 1
Write a C program using serial interrupts to do the following:
  Use the timer 1 8-bit auto-reload mode and set the baud rate at 9600 for serial communication.
  Configure the SCON register for serial communication.
  Start the timer 1.
  Enable the IE register for serial interrupt.
Ask the program to give an acknowledgment ‘RECEIVED’ serially whenever the user presses the space bar key and toggles the pins at port 2 from 00H to FFH.
The value for the SPACEBAR key is 0x20.

## Slide 8
TMOD – Timer 1 8-bit auto-reload: 0010 0000 = 0x20;
TH = 0xFD // 9600 baud rate
SCON = 0101 0000 = 0x50
TR1 = 1
IE = 1001 0000 = 0x90

## Slide 9: Solution
#include <reg51.h>
void main()
{
TMOD=0x20;
TH1=0xFD;
SCON=0x50;
TR1=1;
IE=0x90;
while(1);
}
void ser_intr(void)interrupt 4
{
char c;
c=SBUF;
IE=0x00; //Turning off interrupt to prevent recursion
if(c==0x20)
{
P2=~P2;
SBUF='R'; //Sending back ACK
while(TI==0);
TI=0;
SBUF='E';
while(TI==0);
TI=0;
SBUF='C';
while(TI==0);
TI=0;
SBUF='E’;
while(TI==0);
TI=0;
SBUF='I';
while(TI==0);
TI=0;
SBUF='V';
while(TI==0);
TI=0;
SBUF='E';
while(TI==0);
TI=0;
SBUF='D';
while(TI==0);
TI=0;
}
RI=0;
IE=0x90; //Reactivating the interrupt
}

## Slide 10: Program 2
Write a C program using an interrupt to do the following
1) Receive data serially and send it to P0
2) Read port P1, transmit data serially, and give a copy to P2
3) Make timer 0 generate a square wave of 5 KHz frequency on P0.1
Assume that XTAL = 11.0592 MHz. Use the 9600 baud rate.
Use timer 1 to serially transmit, use timer 0 to generate a square wave

## Slide 11
TH1=0xFD
TH0=0xA4
TMOD=0x22
SCON=0x50
TR0=1
TR1=1
IE=0x92