## Slide 1: Serial Communication

## Slide 2: Introduction
Computers transfer data in two ways:
Parallel
Often 8 or more lines are used to transfer data to a device that is only a few feet away
Serial
To transfer to a device located many meters away, the serial method is used
The data is sent one bit at a time

## Slide 3
Methods
  Synchronous method: transfers a block of data at a time
  Asynchronous method: transfers a single byte at a time
Transmission
  Full Duplex: If data can go both ways at a time
  Half Duplex: If data is transmitted one way at a time

## Slide 4: Baud Rate
Baud Rate: the rate at which information is transferred in a communication channel
To allow data transfer between the PC and an 8051 system without any error, we must make sure that the baud rate of 8051 system matches the baud rate of the PC’s COM port.

## Slide 5: SBUF
SBUF is an 8-bit register.
It acts as a temporary storage location for data being transmitted or received through the serial port.
Transmission
  For a byte data to be transferred via the TxD line, it must be placed in the SBUF register
  The moment a byte is written into SBUF, it is framed with the start and stop bits and transferred serially via the TxD line
Reception
  When the bits are received serially via RxD, the 8051 deframes it by eliminating the stop and start bits, making a byte out of the data received, and then placing it in SBUF.

## Slide 6: SCON
SCON is an 8-bit register used to program the start bit, stop bit, and data bits of data framing
SM0, SM1
They determine the framing of data by specifying the number of bits per character and the start and stop bits.
SM2
This enables the multiprocessing capability of the 8051.

## Slide 7
REN (receive enable)
It is a bit-addressable register. When it is high, it allows 8051 to receive data on the RxD pin
If low, the receiver is disabled
TI (transmit interrupt)
When 8051 finishes the transfer of 8-bit characters.
It raises TI flag to indicate that it is ready to transfer another byte.
TI bit is raised at the beginning of the stop bit.
RI (receive interrupt)
When 8051 receives data serially via RxD, it gets rid of the start and stop bits and places the byte in SBUF.
It raises the RI flag bit to indicate that a byte has been received and should be picked up before it is lost..
RI is raised halfway through the stop bit.

## Slide 8: Transfer Character
1. TMOD register is loaded with the value 20H, indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set the baud rate
2. The TH1 is loaded with one of the values to set the baud rate for serial data transfer
3. The SCON register is loaded with the value 50H, indicating serial mode 1, where an 8- bit data is framed with start and stop bits
4. TR1 is set to 1 to start timer 1
5. TI is cleared
6. The character byte to be transferred serially is written into the SBUF register
7. The TI flag bit is monitored to see if the character has been transferred completely
8. To transfer the next byte, go to step 5

## Slide 9: Receive Character
TMOD register is loaded with the value 20H, indicating the use of timer 1 in mode 2 (8-bit auto-reload) to set baud rate
2. TH1 is loaded to set baud rate
3. The SCON register is loaded with the value 50H, indicating serial mode 1, where an 8- bit data is framed with start and stop bits
4. TR1 is set to 1 to start timer 1
5. RI is cleared
6. The RI flag bit is monitored to see if an entire character has been received yet
7. When RI is raised, SBUF has the byte
8. To receive the next character, go to step 5

## Slide 10: PCON
There are two ways to increase the baud rate of data transfer
- To use a higher-frequency crystal
- To change a bit in the PCON register
PCON register is an 8-bit register
When 8051 is powered up, SMOD is zero
We can set it to high to double the baud rate

## Slide 11: Example 1
#include <reg51.h>
void main(void){
TMOD=0x20; //use Timer 1, mode 2
TH1=0xFA; //4800 baud rate
SCON=0x50;
TR1=1;
while (1) {
SBUF='A'; //place value in buffer
while (TI==0); // watch the TI flag
TI=0;
}
}

## Slide 12: Find the TH1 value needed to have the following baud rates. (a) 9600 (b) 2400 (c) 1200
XTAL = 11.0592 MHz
The machine cycle frequency of 8051 = 11.0592 / 12 = 921.6 kHz, and 921.6 kHz / 32 = 28,800 Hz is frequency by UART to timer 1 to set baud rate.
  (a) 28,800 / 3 = 9600
  (b) 28,800 / 12 = 2400
  (c) 28,800 / 24 = 1200
Time period of each clock tick: T0 = 1/f = 1/28800
Duration of timer: n*T0 (n is the number of clock ticks)
1/9600 = n*T0 = n*1/28800 = 28800/9600 = 3
TH1 =FD