## Slide 1: Practice Questions

## Slide 2: Program 1
Write an 8051 C program to toggle all bits of P2 continuously every 500 ms. Use Timer 1, mode 1 to create the delay.

## Slide 3
#include <reg51.h>
void T1M1Delay(void);
void main(void){
unsigned char x;
P2=0x55;
while (1)
{
P2=~P2;
for (x=0;x<20;x++)
T1M1Delay();
}
}
void T1M1Delay(void){
TMOD=0x10;
TL1=0xFE;
TH1=0xA5;
TR1=1;
while (TF1==0);
TR1=0;
TF1=0;
}
25 ms
T = 25000/1.085 = 23042 us
65536 – 23042 = 42495