## Slide 1: Timer Programs

## Slide 2: Calculating TL and TH
To calculate the values to be loaded into the TL and TH registers, look at the following steps.
Assume XTAL = 11.0592 MHz, we can use the following steps for finding the TH, TL
registers’ values:
1. Divide the desired time delay by 1.085μs.
2. Perform 65536 – n, where n is the decimal value we got in Step1.
3. Convert the result of Step2 to hex, where yyxx is the initial hex value to be loaded into the
timer’s register and
4. Set TL = xx and TH = yy.

## Slide 3: Example – Mode 1
Assume that XTAL = 11.0592 MHz. What value do we need to load the timer’s register if we want to have a time delay of 5 ms ? Show the program for timer 0 to create a pulse width of 5 ms on P2.3.
Solution:
Since XTAL = 11.0592 MHz, the counter counts up every 1.085 us. This means that out of many 1.085 us intervals we must make a 5 ms pulse. To get that, we divide one by the other. We need 5 ms / 1.085μs = 4608 clocks. To Achieve that we need to load into TL and TH the value 65536 – 4608 = EE00H. Therefore, we have TH = EE and TL = 00.

## Slide 4: Example
Assume that XTAL = 11.0592 MHz, write a program to generate a square wave of 2 kHz frequency on pin P1.5.
This is similar to previous example, except that we must toggle the bit to generate the square wave. Look at the following steps.
(a) T = 1 / f = 1 / 2 kHz = 500 us the period of square wave.
(b) 1 / 2 of it for the high and low portion of the pulse is 250 us.
(c) 250 us / 1.085 us = 230 and 65536 – 230 = 65306 which in hex is FF1AH.
(d) TL = 1A and TH = FF, all in hex.

## Slide 5: Example
Assume XTAL = 11.0592 MHz, write a program to generate a square wave of 50 kHz frequency on pin P2.3.
Solution:
Look at the following steps.
(a) T = 1 / 50 = 20 ms, the period of square wave.
(b) 1 / 2 of it for the high and low portion of the pulse is 10 ms.
(c) 10 ms / 1.085 us = 9216 and 65536 – 9216 = 56320 in decimal, and in hex it is DC00H.
(d) TL = 00 and TH = DC (hex).

## Slide 6: Program
Write an 8051 C program to toggle all the bits of port P1 continuously with some delay in between. Use Timer 0, 16-bit mode to generate the delay.
Solution:
#include <reg51.h>
void T0Delay(void);
void main(void)
{
while (1) { //repeat forever
P1=0x55;
T0Delay(); //toggle all the bits of P1
P1=0xAA; // delay unknown
T0Delay();
}
}
void T0Delay()
{
TMOD=0x01; // timer 0 mode 1
TL0=0x00;
TH0=0x35; // load TH and TL
TR0=1; // turn on T0
while (TF0==0); // wait for TF0 to roll over
TR0=0; // turn off T0
TF0=0; // clear TF0
}

## Slide 7: Program
Write an 8051 C program to toggle only bit P1.5 continuously every 50ms. Use Timer 0, mode 1 (16-bit) to create the delay.
Solution:
Assume XTAL=11.0592 MHz=> T=1.085μs Count=50ms/1.085μs =46083
Initial count = 65536-46083 =19453
Count in Hex = 4BFDH
Program
#include <reg51.h>
void T0M1Delay(void);
sbit mybit=P1^5;
void main(void){
while (1){
mybit=~mybit; //toggle P1.5
T0M1Delay();
}}
void T0M1Delay(void){
TMOD=0x01; // Timer 0, mode 1
TL0=0xFD;
TH0=0x4B;
TR0=1;
while (TF0==0);
TR0=0;
TF0=0;
}

## Slide 8: Program
Write an 8051 C program to toggle all bits of P2 continuously every 500 ms. Use Timer 1, mode 1 to create the delay.
Solution:
Assume XTAL=11.0592 MHz=> T=1.085μs Count=500ms/1.085μs =460829 >65536
Let us divide this delay as = 20x25ms, hence count for 25ms can be calculated.
Count = 25ms/1.085μs = 23042
Initial count = 65536 – 23042= 42494
Count in hex = A5FEH
Program
#include <reg51.h>
void T1M1Delay(void);
void main(void){
unsigned char x;
P2=0x55;
while (1){
P2=~P2;
for (x=0;x<20;x++)
T1M1Delay();
}}
void T1M1Delay(void)
{
TMOD=0x10;
TL1=0xFE;
TH1=0xA5;
TR1=1;
while (TF1==0);
TR1=0;
TF1=0;
}

## Slide 9: Program
Write an 8051 C program to toggle only pin P1.5 continuously every 250 ms. Use Timer 0, mode 2 (8-bit auto-reload) to create the delay.
Solution:
Solution: Assume XTAL=11.0592MHz
For the delay of 250ms the count exceeds 256. hence, count for 25μs is calculated and count is 23
Therefore for 250ms =>25μs × 250 × 40 = 250 ms
Program
#include <reg51.h>
void T0M2Delay(void);
sbit mybit=P1^5;
void main(void){
unsigned char x,y;
while (1) {
mybit=~mybit;
for (x=0;x<250;x++)
for (y=0;y<36;y++) //we put 36, not 40
T0M2Delay();
}}
void T0M2Delay(void){
TMOD=0x02;
TH0=E9;
TR0=1;
while (TF0==0);
TR0=0;
TF0=0;
}

## Slide 10: Program
Write an 8051 C program to create a frequency of 2500 Hz on pin P2.7. Use Timer 1, mode 2 to create delay.
Solution:
XTAL = 11.0592MHz, given freq of wave = 2500Hz
Time Period=1/2500Hz = 400μs
Ton=Toff= 400μs /2 = 200μs
Count = 200μs / 1.085μs = 184
Initial count =256-184 = 72
In hex = 48H
Program
#include <reg51.h>
void T1M2Delay(void);
sbit mybit=P2^7;
void main(void){
unsigned char x;
while (1) {
mybit=~mybit;
}
T1M2Delay();
}
}
void T1M2Delay(void){
TMOD=0x20;
TH1=0x48;
TR1=1;
while (TF1==0);
TR1=0;
TF1=0;

## Slide 11: Counters
Assume that a 1-Hz external clock is being fed into pin T1 (P3.5). Write a C program for counter 1 in mode 2 (8-bit auto reload) to count up and display the state of the TL1 count on P1. Start the count at 0H.
Program:
#include <reg51.h>
sbit T1=P3^5;
void main(void){
T1=1;
TMOD=0x60;
TH1=0;
while (1) {
do {
TR1=1;
P1=TL1;
} while (TF1==0);
TR1=0;
TF1=0;
}
}

## Slide 12: Counters
Assume that a 1-Hz external clock is being fed into pin T0 (P3.4). Write a C program for counter 0 in mode 1 (16-bit) to count the pulses and display the state of the TH0 and TL0 registers on P2 and P1, respectively.
Program:
#include <reg51.h>
sbit T0=P3^4;
void main(void){
T0=1;
TMOD=0x05;
TL0=0
TH0=0;
while (1) {
do {
TR0=1;
P1=TL0;
P2=TH0;
} while (TF0==0);
TR0=0;
TF0=0;
}
}

## Slide 13: Example – Mode 2
Assume XTAL = 11.0592 MHz, find the frequency of the square wave generated on pin P1.0 in the following program
In mode 2 we do not need to reload TH since it is auto-reload.
Now (256 - 05) × 1.085 us = 251 × 1.085 us = 272.33 us is the high portion of the pulse.
Since it is a 50% duty cycle square wave, the period T is twice that; as a result
T = 2 × 272.33 us = 544.67 us and the frequency = 1.83597 kHz

## Slide 14: Example
Write a program to generate a square wave of frequency 72Hz on pin P1.0.
Solution: Assume XTAL=11.0592MHz. With TH=00, the delay generated is
256 x 1.085 μs = 277.76 μs. therefore to generate a delay of (1 / 72) = 138.88ms, the count
to be loaded is 250 x 2=500.
That is T = 2 (250 × 256 × 1.085 μs) = 138.88ms, and frequency = 72 Hz