## Slide 1: Timers and Counters

## Slide 2: STEPS TO CALCULATE VALUES TO LOAD INTO TH-TL TO GENERATE DESIRED DELAY
(XTAL = 11.0592 MHz)
1. Divide the desired time delay by 1.085 us
2. Perform 65536 – n, where n is the decimal value we got in Step 1
3. Convert the result of Step 2 to hex
4. Set TL = xx and TH = yy

## Slide 3: EXAMPLE 1
Generate Delay =10ms with Clock frequency= 11.0592 MHz, using Timer0 in mode1.
Step 1: Divide the desired time delay by 1.085 us
Count =10 ms/ 1.085 us=9216
Step 2: Perform 65536 – n
65536-9216=56320
Step 3: Convert the result to hex
DC00H
Step 4: Set TL = xx and TH = yy
TH0=DC and TL0=00.

## Slide 4: EXAMPLE 2
Generate Delay =1ms with Clock frequency= 11.0592 MHz, using Timer0 in mode1.

## Slide 5: SOLUTION
N = 1ms/1.085μs ≈ 922.
M = 65536-922 = 64614 (decimal).
64614 in Hexadecimal = FC66h.

## Slide 6: EXAMPLE 3
Assuming XTAL = 11.0592 MHz, write a program to generate a square wave of 50 Hz frequency on pin P2.3.

## Slide 7: SOLUTION
T = 1/50 Hz = 20 ms
1/2 of it for the high and low portions of the pulse = 10 ms
10 ms / 1.085 us = 9216
65536 - 9216 = 56320 in decimal = DC00H
TL = 00 and TH = DCH
The calculation for 12MHz crystal uses the same steps

## Slide 8: EXAMPLE 4
Write an 8051 C program to create a frequency of 2500Hz on pin P2.7. Use Timer 1, mode 2 to create the delay.

## Slide 9: SOLUTION
Given frequency: 2500Hz
T = 1/2500 Hz = 400ms
1/2 of it for the high and low portions of the pulse = 200ms
200ms / 1.085 us = 184.33≈184
256 - 184 = 72 in decimal = 48H
TH = 48H